December 30, 2009

Ms. Cindy Garner

Enforcement Administrator

NPDES Enforcement Section

Arkansas Department of Environmental Quality

5301 North Shore Dr

North Little Rock, Arkansas 72118

RE:  Storm water Blending December 24, 2009 thru December 25, 2009

Russellville City Corporation Pollution Control Works

NPDES Permit No.  AR0021768  AFIN 58-0015

Dear Ms. Garner:

In an attempt to save the City Corporation Pollution Control Works from becoming hydraulically overloaded,  we would provide the following data for the storm water blending event that occurred at the Pollution Control Works, Thursday December 24, 2009 and ending Friday December 25, 2009.   As was conveyed in the initial report this blending was due to excessive storm events experienced in the area.

We would offer the following results:

Gallons blended:  3,553,000 gallons estimated.

## Thursday, December 24, 2009

Total Suspended Solids                   128.0  mg/l            CL2       0.11 mg/l

Dissolved Oxygen		  6.3  mg/l	pH	 6.71

Ammonia			 .29   mg/l	BOD 	 14.3 mg/l

Fecals			           5450/100ml

## Friday, December 25, 2009

Total Suspended Solids                    53.0  mg/l            CL2        0.25 mg/l

Dissolved Oxygen		10.1  mg/l	pH	6.79

Ammonia			1.10  mg/l	BOD 	10.8 mg/l

Fecals			               22/100ml

Sincerely,

Craig Noble

General Manager

cc:	Scott Ketchum

Randy Bradley

File