February 24, 2010

Ms. Cindy Garner

Enforcement Administrator

NPDES Enforcement Section

Arkansas Department of Environmental Quality

5301 North Shore Dr

North Little Rock, Arkansas 72118

RE:  Storm water Blending January 29, 2010 thru February 17, 2010

Russellville City Corporation Pollution Control Works

NPDES Permit No.  AR0021768  AFIN 58-0015

Dear Ms. Garner:

In an attempt to save the City Corporation Pollution Control Works from becoming hydraulically overloaded,  we would provide the following data for the storm water blending event that occurred at the Pollution Control Works, Friday January 29, 2010 and ending Wednesday February 17, 2010.   As was conveyed in the initial report this blending was due to excessive storm events experienced in the area.

We would offer the following results:

Gallons blended:  89,199,000 gallons estimated.

## Friday, January 29, 2010

Total Suspended Solids                      9.3  mg/l            CL2         0.18 mg/l

Dissolved Oxygen		  9.9  mg/l	pH	 7.03

Ammonia		             0.09   mg/l	BOD 	 3.6 mg/l

Fecals			             424/100ml

## Monday, February 1, 2010

Total Suspended Solids                    10.8  mg/l            CL2        0.16 mg/l

Dissolved Oxygen		  9.8  mg/l	pH	6.78

Ammonia			1.75  mg/l	BOD 	8.7 mg/l

Fecals			               12/100ml

## Tuesday, February 2, 2010

Total Suspended Solids                    12.1  mg/l            CL2        0.13 mg/l

Dissolved Oxygen		  9.1  mg/l	pH	6.83

Ammonia			1.68  mg/l	BOD 	10.7 mg/l

Fecals			               24/100ml

## Wednesday, February 3, 2010

Total Suspended Solids                    13.7  mg/l            CL2       0.12 mg/l

Dissolved Oxygen		  9.2  mg/l	pH	 6.94

Ammonia		             1.43   mg/l	BOD 	 15.2 mg/l

Fecals			             290/100ml

## Thursday, February 4, 2010

Total Suspended Solids                    14.5  mg/l            CL2        0.15 mg/l

Dissolved Oxygen		  9.1  mg/l	pH	6.93

Ammonia			1.28  mg/l	BOD 	11.3 mg/l

Fecals			           3570/100ml

## Friday, February 5, 2010

Total Suspended Solids                    20.5  mg/l            CL2        0. 04mg/l

Dissolved Oxygen		  8.1  mg/l	pH	6.83

Ammonia		             2 .79  mg/l	BOD 	25.7 mg/l

Fecals			        20,100/100ml

## Monday, February 8, 2010

Total Suspended Solids                    15.3  mg/l            CL2       0.11 mg/l

Dissolved Oxygen		  9.3  mg/l	pH	 6.90

Ammonia		             1.49   mg/l	BOD 	 10.6 mg/l

Fecals			          9,100/100ml

## Tuesday, February 9, 2010

Total Suspended Solids                    15.3  mg/l            CL2        0.13 mg/l

Dissolved Oxygen		10.0  mg/l	pH	6.96

Ammonia			2.19  mg/l	BOD 	12.6 mg/l

Fecals			          1,100/100ml

## Wednesday, February 10, 2010

Total Suspended Solids                    25.7  mg/l            CL2        0.11 mg/l

Dissolved Oxygen		  9.8  mg/l	pH	6.88

Ammonia			1.82  mg/l	BOD 	13.6 mg/l

Fecals			          9,400/100ml

## Thursday, February 11, 2010

Total Suspended Solids                    28.0  mg/l            CL2        0.20 mg/l

Dissolved Oxygen		10.1  mg/l	pH	 6.95

Ammonia		               1.58  mg/l	BOD 	 14.3 mg/l

Fecals			          3,100/100ml

## Friday, February 12, 2010

Total Suspended Solids                    41.0  mg/l            CL2        0.21 mg/l

Dissolved Oxygen		  9.7  mg/l	pH	6.96

Ammonia			1.17  mg/l	BOD 	15.6 mg/l

Fecals			             600/100ml

## Monday, February 15, 2010

Total Suspended Solids                  142.3  mg/l            CL2        0.02 mg/l

Dissolved Oxygen		  9.5  mg/l	pH	7.13

Ammonia			3.25  mg/l	BOD 	26.7 mg/l

Fecals			        11,500/100ml

## Tuesday, February 16, 2010

Total Suspended Solids                    71.3  mg/l            CL2       0.01 mg/l

Dissolved Oxygen		  9.8  mg/l	pH	 7.27

Ammonia		               4.0   mg/l	BOD 	 20.4 mg/l

Fecals			          6,000/100ml

## Wednesday, February 17, 2010

Total Suspended Solids                     63.3mg/l	CL2        0.21 mg/l

Dissolved Oxygen		 10.4mg/l	pH	7.28

Ammonia		 	 2.88mg/l	BOD 	20.5 mg/l

Fecals			             440/100ml

Sincerely,

Craig Noble

General Manager

cc:	Scott Ketchum

Randy Bradley

File