February 3, 2010

Ms. Cindy Garner

Enforcement Administrator

NPDES Enforcement Section

Arkansas Department of Environmental Quality

5301 North Shore Dr

North Little Rock, Arkansas 72118

RE:  Storm water Blending January 23, 2010 thru January 27, 2010

Russellville City Corporation Pollution Control Works

NPDES Permit No.  AR0021768  AFIN 58-0015

Dear Ms. Garner:

In an attempt to save the City Corporation Pollution Control Works from becoming hydraulically overloaded,  we would provide the following data for the storm water blending event that occurred at the Pollution Control Works, Saturday January 23, 2010 and ending Wednesday January 27, 2010.   As was conveyed in the initial report this blending was due to excessive storm events experienced in the area.

We would offer the following results:

Gallons blended:  17,204,000 gallons estimated.

## Monday, January 25, 2010

Total Suspended Solids                      9.0  mg/l            CL2       0.18 mg/l

Dissolved Oxygen		  9.8  mg/l	pH	 7.04

Ammonia		             1.55   mg/l	BOD 	 8.4 mg/l

Fecals			            660 /100ml

## Tuesday, January 26, 2010

Total Suspended Solids                    11.9  mg/l            CL2        0.23 mg/l

Dissolved Oxygen		  9.9  mg/l	pH	6.97

Ammonia			1.30  mg/l	BOD 	7.3 mg/l

Fecals			             720/100ml

## Wednesday, January 27, 2010

Total Suspended Solids                      8.9  mg/l            CL2        0.19 mg/l

Dissolved Oxygen		10.1  mg/l	pH	7.05

Ammonia			  .79  mg/l	BOD 	7.6 mg/l

Fecals			             105/100ml

Sincerely,

Craig Noble

General Manager

cc:	Scott Ketchum

Randy Bradley

File