June 16, 2008

Ms. Cindy Garner

Enforcement Administrator

NPDES Enforcement Section

Arkansas Department of Environmental Quality

5301 North Shore Dr

North Little Rock, Arkansas 72118

RE:  Storm water Blending June 9, 2008 thru June 10, 2008

Russellville City Corporation Pollution Control Works

NPDES Permit No.  AR0021768

Dear Ms. Garner:

In conformance with Consent Administrative Order LIS 06-114 we would provide the following data for the storm water blending event that occurred at the Pollution Control Works, Monday June 9, 2008 ending Tuesday June 10, 2008, as conveyed in the initial reports this blending was due to excessive storm events experienced in the area.

Please see the following results:

Gallons blended:     1,309,000 gallons estimated.

# Monday June 9, 2008

Total Suspended Solids          	  6.8   mg/l	CL2		0.29 mg/l

Dissolved Oxygen		   7.5  mg/l	pH		6.41

Ammonia			  .13   mg/l	BOD 		6.8 mg/l

Fecals			               13/100ml

# Tuesday June 10, 2008

Total Suspended Solids        	13.2   mg/l	CL2		0.62 mg/l

Dissolved Oxygen		   7.6  mg/l	pH		6.63

Ammonia			1.36   mg/l	BOD 		2.9 mg/l

Fecals			                 1/100ml

Sincerely,

Craig Noble

General Manager

cc:	Eddie Duvall

Randy Bradley

File