February 2, 2012

Alan Anderson

NPDES Enforcement Section

Arkansas Department of Environmental Quality

5301 North Shore Dr

North Little Rock, Arkansas 72118

RE:  Storm water Blending January 25, 2012 thru January 26, 2012

Russellville City Corporation Pollution Control Works

NPDES Permit No.  AR0021768  AFIN 58-0015

Dear Mr. Anderson:

In an attempt to save the City Corporation Pollution Control Works from becoming hydraulically overloaded,  we would provide the following data for the storm water blending event that occurred at the Pollution Control Works, Wednesday January 25, 2012 and ending Thursday January 26, 2012.   As was conveyed in the initial report this blending was due to excessive storm events experienced in the area.

We would offer the following results:

Gallons blended:  5,049,000 gallons estimated.

## Wednesday,  January  25, 2012

Total Suspended Solids                   10.3  mg/l             CL2        0.34 mg/l

Dissolved Oxygen	 	 7.4  mg/l	pH	6.3

Ammonia		             0.11  mg/l	BOD 	5.1 mg/l

Fecals			         Lab accident

## Thursday,  January 26, 2012

Total Suspended Solids                    24.3  mg/l             CL2        0.35 mg/l

Dissolved Oxygen	 	 9.9  mg/l	pH	6.55

Ammonia		              2.43  mg/l	BOD 	30.7 mg/l

Fecals			            215/100ml

Sincerely,

Craig Noble

General Manager

cc:	Ricky Biffle

Randy Bradley

File